## Slide 1: Surface Alpha Interactions in PPC HPGe Detectors: Maximizing Sensitivity of 76Ge 0νββ Searches
Julieta Gruszko
PhD Defense
University of Washington
Department of Physics
Aug. 4, 2017

## Slide 2: Outline
Introduction to Neutrinoless Double Beta Decay
PPC Detectors and Low-Background Physics
Surface Alpha Identification with DCR
PPC Response Measurement with TUBE
Alpha Backgrounds in the Majorana Demonstrator

## Slide 3: Introduction to 0νββ

## Slide 4: Neutrino Basics
Light, neutral particles
Very low interaction rates
Only and in SM
3 flavors, 3 mass states
Tiny masses (<2 eV), unknown mass hierarchy
Notes: - Solar neutrino flux on earth is ~7E10 (70 billion) particles /cm2/sec
- neutrinos are 5 to 6 orders of magnitude (1 million times) lighter than other particles

## Slide 5: Neutrino Mass
Mass must be BSM
Two ways to give the neutrino mass:
  Dirac: Majorana:
4 mass-degenerate states:
non-interacting
not in SM
makes l+
makes l-
2 mass-degenerate states:
makes l+
makes l-

## Slide 6: Why Majorana Neutrinos?
Combine the two mass terms in a “see-saw mechanism”:
Solves the neutrino mass hierarchy problem, implications for matter/anti-matter asymmetry
4
Dirac Neutrino
2
Majorana Neutrino
2
Majorana Neutrino
Splitting due to Majorana mass

## Slide 7: Neutrinoless Double Beta Decay
2νββ: a rare SM process that occurs in some nuclei
If neutrinos are Majorana, 0νββ could occur
Lepton number conservation is violated
Δl = 2
e-
W-
νM
e-
W-
A, Z
A, Z+2
e-
W-
νe
e-
W-
A, Z
A, Z+2
νe

## Slide 8: The 0νββ Rate
Rate depends on mixing angles and phases, neutrino mass, and mass hierarchy
Uncertainties in:
  mββ: lightest ν mass, phases, hierarchy
  Nuclear matrix elements
Figure courtesy of A. Schubert
Notes: 1 sigma on mixing angles
Split into two slides?
introduce mbb after rate
rate is the thing we measure, and then extract mbb
explain rate

## Slide 9: How to Detect 0νββ
Don’t detect neutrinos directly
Ignore the neutrinos, measure the rest of the energy
Current limits:
T1/2 > 1025 years
Need a large mass, high efficiency, low background
Notes: avogradro’s number = 6E23 helps here

## Slide 10: The Majorana Demonstrator
The Majorana Demonstrator (MJD) is an array of enriched and natural germanium detectors that will search for the 0νββ-decay of 76Ge.
Goals:
Demonstrate backgrounds low enough to justify building a tonne scale experiment.
Establish feasibility to construct & field modular arrays of Ge detectors.
Searches for additional physics beyond the standard model
Background goal: 3 counts/ROI/t/y after analysis cuts
  Qββ = 2.039 MeV
Prototype taking data: July 2014 – April 2016
Operations: M1 from May 2015, M2 from July 2016
Photo by Matt Kapust

## Slide 11: The Present and Future of 76Ge 0νββ
Parallel efforts using different approaches
  MJD: Underground electroformed copper and other ultra-clean materials, mostly passive shielding
  GERDA: Slightly higher-background materials, active shielding with LAr
Combine best techniques for tonne-scale experiment
  LEGEND Collaboration formed October 2016
The Majorana Demonstrator
GERDA

## Slide 12: Discovery, Background, and Exposure
Figure courtesy of J. Detwiler
Notes: Take your time!
Start with plot axes
We’re looking for where lines cross
GERDA and MJD will work together to build tonne-scale Ge detector - LEGEND
Start with just the blue lines? add sensitivity

## Slide 13: Alpha Backgrounds
Short range, high energy, detected poorly
Radon is the biggest problem
5.3 MeV
Notes: ~20 um in Ge, ~10um in copper
Mention Rn plate-out, can be full energy (if found on detector surface or

## Slide 14: The Majorana Detector Unit
Developed procedure & QA, trained MJD detector-assembly workforce
Holds detector, cabling, front-end electronics

## Slide 15: PPC Detectors and Low-Background Physics

## Slide 16: HPGe Detectors
γ
One big Ge diode, fully depleted
Charge proportional to energy
Electron and hole fractions depend on position
In MJ, use enriched Ge (88% 76Ge)
+
-
+
-
Charge Integration

## Slide 17: HPGe Detectors
γ
One big Ge diode, fully depleted
Charge proportional to energy
Electron and hole fractions depend on position
In MJ, use enriched Ge (88% 76Ge)
+
-
+
-
Charge Integration

## Slide 18: PPC Detectors
Better energy resolution, lower thresholds
Pulse shape highly dependent on position  multi-site PSD
2/0νββ is intrinsically single-site
Decay due to electronics
Notes: First developed about 15 years ago, this is the first generation of large-scale experiments to use them
Still work to be done to completely understand their behavior

## Slide 19: Pulse Shape Discrimination with A/E
A = maximum current, E = energy
Multi-site events have low A/E
Near-p+ events have high A/E
Detector Drift Times
r (mm)
z (mm)
Drift time (ns)
Time (μs)
Current (ADC/ns)
Voltage (ADC)
Normal SSE
MSE
Near-p+ SSE

## Slide 20: Surface Events
Canberra BEGe Geometry
MJD natural detectors
GERDA enriched detectors
ORTEC Geometry
MJD enriched detectors
n+ contact: .5 mm diffused lithium
  α’s don’t penetrate
p+ contact: .3 μm implanted boron
  α’s barely lose energy
  Very fast drift, easy to ID with PSD
Passivated surface: very thin, but poor charge collection

## Slide 21: Identifying Surface Alphas with DCR

## Slide 22: α Background in MJD
The Preliminary MJD Spectrum
With data cleaning, muon, and mult. cuts
+ MSE rejection
2νββ
Clear 210Po peak
Extra structure below 3 MeV
ROI backgrounds far above level expected from assay
Dominant background in ROI

## Slide 23: GERDA’s α Background
Approx. 1/2 of ROI events after LAr veto
Not 210Pb supported,
  t1/2 = 138 days
Smaller passivated surface
  Fewer α events
  All passivated surface events have high A/E
The GERDA Collaboration. Background-free search for neutrinoless double-decay of 76Ge with GERDA. Nature, 544(7648):47–52, 04 2017.
A/E
Counts
GERDA Spectrum and PSD
Energy (keV)
ORTEC
BEGe
n+
passivated
p+

## Slide 24: Detector Geometry and α Rejection
High A/E is a fiducial volume cut– removes bulk events
Would be better to cut based on specific surface behavior
Passivated Region
ORTEC Drift Time Map
z (mm)
r (mm)
Drift Time (ns)
r (mm)
Drift Time (ns)
z (mm)
BEGe Drift Time Map

## Slide 25: Passivated Surface Pulse Shapes
Some of the charge collected normally
Delayed charge recovery (DCR) from:
  Surface drift of electrons on surface
  Near-surface hole trapping and slow re-release
Simulated with siggen
r = 11.5 mm
r = 21.5 mm
r = 1.5 mm
Siggen developed by David Radford
Simulations by Susanne Mertens

## Slide 26: The DCR PSD Parameter
Correct for decay from electronics
Measure slope of tail
Cut events with high DCR
Keep 99% of γ calibration events
α
γ
Publication in preparation

## Slide 27: Preliminary Tests in MJD
Events cut:
  10% of single-site calibration events between 1 and 2.38 MeV
  16.4% with energy between 1 and 2 MeV
  88.4% with energy between 2 and 3 MeV
Need dedicated α data to validate
MJD Preliminary Data,
Enriched Detectors

## Slide 28: Measuring PPC Response with TUBE

## Slide 29: The TUM Upside-Down BEGe (TUBE) Scanner
First joint work between GERDA and MJD groups
Adapted existing alpha scanning system to scan MJD detector
First assembled Sept. 2016, data taken Feb. – June 2017
Questions:
  Energy spectrum
  E vs. R
  DCR vs. R
  Charge loss mechanism
  A/E and DCR complementarity
  DCR α rejection power
7cm

## Slide 30: TUBE Measurements
241Am source:
  5.486 MeV α, 20 keV line-width
  40 kBq, 65 events/hour
  1 mm collimator  1.8mm spot size
Scanned every 1.5 mm, 65° angle of incidence, some extra half-positions
Distances from point-contact are radial
24 hours per scan position
65°

## Slide 31: Alpha Energy
r = 24 mm
p+ events
30 mm
FWHMgaus = 21 keV
FWHM = 56 keV
TUBE Energy Spectra

## Slide 32: E vs. R
Passivated surface:
r = aE4+rp
Can’t just be electron loss!
E vs. R
Fitting to R vs. E
WP at Passivated Surface
Notes: Fit with a single free parameter, scaling parameter a
Later, I’ll show you how this can be used to model alpha backgrounds

## Slide 33: Alpha DCR
r = 24 mm
p+ events
60 mm
30 mm
TUBE DCR Distributions

## Slide 34: Unexpected Result: DCR Stability
DCR values increase over time, high α rate appears to cause charge build-up. Drops when source is removed from surface.
2 leading theories about mechanism, can test in the future
Not relevant for MJD (rate is ~5 orders of magnitude lower)
r = -15mm
r = -9mm
r = -7.5mm
r = -4.5mm
r = -30mm
Higher integrated rate,
larger increase in DCR
DCR of Repeated Positions
DCR over Time, with α Rate:
DCR (ADC/ns)
DCR (ADC/ns)

## Slide 35: DCR vs. R
2 – 3.5% of event energy is collected as delayed charge at positions more than 8mm away from p+ contact:
Events near p+ contact have rapidly falling DCR
DCR vs. R
Delayed Charge Fraction vs. R

## Slide 36: Charge Loss Mechanism
DCR increases with energy and radius
  Hole recovery dominates DCR mechanism
  Suggests near-surface trapping & rerelease
Delayed Charge Fraction vs. |R|
WP at Passivated Surface

## Slide 37: A/E and DCR Complementarity
All positions fall above 99.9% on either A/E or DCR
We should be able to remove ~all α events w/ minimal sacrifice
99.9% Bulk
DCR Acc.
99.9% Bulk
A/E Acc.
A/E (arb)
DCR (arb)
30 mm

## Slide 38: A/E and DCR α Rejection Power
Suggests that the transition is at ~8mm
Publication in preparation
5σ DCR
99.9% Bulk
DCR Acc.
5σ A/E
99.9% Bulk
A/E Acc.
99% A/E and DCR
DCR or A/E (σ)
Distance from P-contact (mm)
BEGe passivated surface

## Slide 39: Alpha Backgrounds in MJD

## Slide 40: DCR and Alpha Backgrounds
MJD Preliminary Spectrum, Enriched Detectors
DCR reduces ROI background rate by a factor of 31
After cut, ROI backgrounds are within uncertainty of 3 counts/ROI/t/y
At current exposure, improves 0νββ limit by 24%
After 5 years of running, improves sensitivity by a factor of 3
  Corresponds to $8.5m-worth more 76Ge
With data cleaning, muon, and mult. cuts
+ MSE rejection
+ α rejection
Notes: 14 more detectors

## Slide 41: Pin-point Background Modeling
Using TUBE α spectrum, distinguish between background sources
65°
θ
or
Completely analytic, for now
A few caveats:
rescale energies (210Po, not 241Am)
p+ deadness fraction
p+ α peak shape

## Slide 42: Testing Two Models
Constant Across Surface
Can immediately discard constant model
MJD enr. data
Projected α spec.
Point Source Above Surface
Counts (arb)
0 < h < 20 mm

## Slide 43: Fitting to α Source
Just two free parameters: height and overall scaling (α rate)
Strongly suggests plastic bushing is responsible
Full simulation needed
Fitting α Spectrum to MJD Data
MJD enr. data
Projected α spec.
h ~3.8 mm
3.65 mm
4.92 mm

## Slide 44: Conclusion
I have characterized PPC charge collection near the passivated surface and identified the cause of the observed delayed charge recovery.
Using the DCR cut, the MJD background has been reduced by a factor of ~30, improving sensitivity by a factor of 3.
Using TUBE results, we can model the spectrum of α events, even identify their source. Then high-α background parts can be removed in MJD and avoided in LEGEND.
Improved understanding of PPC behavior can drastically improve our ability to search for rare events and BSM physics, like 0νββ.

## Slide 45: Thank You to:
the money:
  UW Physics, ARCS, NSF, and DOE
the Majorana and GERDA Collaborations, and all of the staff at CENPA
the MJ groups at UW and at TUM
my committee, and particularly to Jason
all of my family and friends
This material is based upon work supported by the National Science Foundation Graduate Research Fellowship under Grant No. 1256082. Any opinion, findings, and conclusions or recommendations expressed in this material are those of the authors(s) and do not necessarily reflect the views of the National Science Foundation.
This material is based upon work supported by the U.S. Department of Energy, Office of Science, Office of Nuclear Physics, the Particle Astrophysics and Nuclear Physics Programs of the National Science Foundation, and the Sanford Underground Research Facility.

## Slide 46: Extra Slides

## Slide 47: Unexpected Result: DCR Stability
Two potential causes
Deep trap filling: Surface channel formation:
E
+
-
+
Test under changing temperature to distinguish
-
-

## Slide 48: MJD Alpha Backgrounds
Identified high α-rate detectors
210Po is Pb-supported
But α rejection is already good, and can still be improved
7 detectors have rates inconsistent with the average